## Slide 1: Training on Basic to Intermediate CCNA

## Slide 2: Training outline
Layered Architecture
Ethernet networking and topologies
IP addressing and subnetting
Communication media
Cisco IOS and CLI
Layer 2 switching
  VLAN, Trunking, VTP, STP
Layer 3 services
  Routing, DHCP, ACL, NAT
Troubleshooting utilities
Demonstrations

## Slide 3: Layered approach
Why reference model?
  Communication b/n different vendors
  OSI reference model
Why layered approach?
  Reduces complexity: divides into smaller and simpler components
  Defines functions of each layer, prevents changes in one layer from affecting other layers

## Slide 4: IP Addressing
What is IP address ?
Classful IP addressing
Subnetting
Classless Inter-Domain Routing (CIDR)
Solutions to Scaling IP Address Space

## Slide 5: What is IP address ?
Physical
Link
Network
Transport
Application
Physical
Link
Network
Transport
Application
Physical
Link
Network
Transport
Application
HTTP, FTP, SMTP, TELNET, etc
TCP, UDP
IP
PPP, Ethernet
www.cs.umass.edu
128.119.240.46
Host 1
Host 2
Host 3

## Slide 6
Classful IP Addressing
Dotted-Decimal Notation
32 bits

## Slide 7
0.0.0.0: default route, used only during Startup
127.0.0.0: loopback, test TCP/IP for IPC on local machine
host all 0: this host
host all 1: limited broadcast (local net)
Special Cases:

## Slide 8
27-2 = 126 networks
224-2 = 16,777,214 hosts / network
214 = 16,384 networks
216-2 = 65,534 hosts / network
221 = 2,097,152 networks
28-2 = 254 hosts / network
/8
/16
/24
Class D: (IP Multicasting)
1110
0 4
Class E: (Experimental use)
1111
0 4

## Slide 9
Class A
Class B
Class C
D
IP Address Space
E
50 %
25%
12.5%
6.25%
232 = 4,294,967,296 addresses
Partition of the Classful IP Addresses

## Slide 10
Limitations to Classful Addressing
Running out of address space soon
232 = 4,294,967,296 addresses
Class boundaries did not foster
efficient allocation of address space
Lack of address class to support medium size company
-- Class B: 65534 hosts/network, too big!
-- Class C: 254 hosts/network, too small!
-- Use multiple class C addresses,
increase routing table!

## Slide 11
Subnetting
Idea: Add one more level (subnet number) to the class hierarchy
Subnet Mask

## Slide 12
Subneting Advantages:
routing table does not grow
flexibility for local network
administrator
hide route flapping from
outside routers

## Slide 13
Subnet Design Considerations
1) How many total subnets does the organization need today?
2) How many total subnets will the organization need in the
future?
3) How many hosts are there on the organization's largest subnet
today?
4) How many hosts will there be on the organization's largest
subnet in the future?

## Slide 14
Given : An organization has been assigned the network number
140.25.0.0/16 and it needs to create a set of subnets that
supports up to 60 hosts on each subnet.
Subnet Design Example
1. Defining the Subnet Mask / Extended-Prefix Length
26-2 = 62, no room for expansion; 27-2 = 126

## Slide 15
2. Defining Subnet Numbers
Base Net:10001100.00011001.00000000.00000000=140.25.0.0/16
SN#0:10001100.00011001.00000000.00000000=140.25.0.0/25
SN #1:10001100.00011001.00000000.10000000=140.25.0.128/25
……………………………………………………………………..
SN #511:10001100.00011001.11111111.10000000=140.25.255.128/25
3. Defining Hosts Addresses for Each Subnet
SN #3: 10001100.00011001.00000001.1 0000000 = 140.25.1.128/25
Host #1: 10001100.00011001.00000001.1 0000001 = 140.25.1.129/25
Host #2: 10001100.00011001.00000001.1 0000010 = 140.25.1.130/25
………………………………………………………………………….
Host #127: 10001100.00011001.00000001.1 1111110 = 140.25.1.193/25
4. Defining the Broadcast Address for Each Subnet
Subnet #3 broadcast: (all 1's host address)
10001100.00011001.00000001.1 1111111 = 140.25.1.255
Subnet Design Example Cont’d

## Slide 16
Variable Length Subnet Masks (VLSM)
Classless Inter-Domain Routing (CIDR) very similar
Allow more efficient use of network addresses
210-2=1022 hosts/subnet, waste of addresses when host number small
26-2=62 hosts/subnet, good for small subnet

## Slide 17
Helps to reduce routing table size (Route Aggregation)
Subnets can be further
recursively divided into
sub-2 nets and so on
A subnet summarizes all
its lower level hierarchies
into a single advertisement

## Slide 18
VLSM Design Considerations
1) How many total subnets does this level need today?
2) How many total subnets will this level need in the future?
3) How many hosts are there on this level's largest subnet today?
4) How many hosts will there be on this level's largest subnet be
in the future?
At each level, ask the following questions:
e.g. 5-college

## Slide 19: OSI and TCP/IP layers
User interface to different
application layer protocols
End-to-end connection
Segmentation
Device addressing
Best path selection
Media Access Control
Flow and error control
Data translation
Compression
Code formatting
Electrical
Mechanical
Procedural
Setting up, terminate
Keeps d/t data separate
Host-to-host
Internet
TCP/IP
OSI
Application
Network access

## Slide 20: Encapsulation and De-capsulation
Data
Segment
Packet
Frame
Bits
PDU
TH
Sg1
IH
FH
FT
100101110010…
Communication media
IH
FH
TH
Sg1
FT
Sg2
Sg3
Data

## Slide 21: TCP and UDP
TCP
Connection-oriented: 3 way handshake
Reliable: ACK, retransmission
Congestion control- Windowing
Uses sequence Numbers
UDP
Connection-less
Unreliable
Best effort
Segments may arrive out of order
A
B
SYN
SYN-ACK
ACK
3way hand shake
ACK 4
1
2
3
x
4
5
6
ACK 5
Window size
5
6
retransmission
A
B
x
No ACK
No retransmission for lost data

## Slide 22: Port numbers
21
23
80
53
69
110
TCP
UDP
FTP
Telnet
HTTP
DNS
TFTP
POP
Port numbers
Application layer
Transport layer
Used at the transport layer to identify application layer protocols
Ports <1024: well known port numbers
6
17
IP
Protocol numbers

## Slide 23: Cisco IOS
IOS-Internetwork Operating System
kernel of Cisco routers and switches that provides routing, switching & other internetworking functions
RAM- running configuration, lost if power is off
FLASH-storage for IOS
NVRAM- start-up configuration
ROM-stores router’s bootstrap, POST, ROMMON
Running configuration vs startup configuration

## Slide 24: Cisco IOS (Cont’d)
POST: Diagnostic utility
  Tests the hardware to verify that all components are operational and present
  Checked at the first step of the boot sequence
Bootstrap:
  Finds where IOS program is located, uses the value in config reg
  Loads IOS image
  Default being from flash memory, from TFTP also possible
ROMMON:
  Used when bootstrap fails to load the IOS
  provides a command-line environment used to perform some minimal configuration tasks (downloading IOS image using TFTP, recovering a lost password, etc)
CLI is used to access the IOS
.

## Slide 25: Booting procedure of Cisco router
Power on
a router
Look for
IOS
POST
passed?
IOS found?
Load IOS
To RAM
Valid
Config in
flash?
Reload
Config to
RAM
Enter
Setup
mode
Exit
ROMMON
Yes
No
No
No
Yes
Yes

## Slide 26: Cisco Switch parts
Front View of 2960 switch
Rear View of 2960 switch
Sys status LEDs
10/100 ports (RJ-45)
gig ports (RJ-45)
gig ports (SFP)
Combo ports
Port LEDs
Console cable
Fan
Power input

## Slide 27: Command Line Interface (CLI)
Cisco IOS user interface
When start a session on the switch, we begin in user EXEC mode
  Switch>
  Switch>?
  Exec commands:
  enable Turn on privileged commands
  exit Exit from the EXEC
  logout Exit from the EXEC
  ping Send echo messages
  show Show running system information
  telnet Open a telnet connection

## Slide 28: CLI Cont’d
To have access to all commands: enter privileged EXEC mode
Switch>en?
enable
Switch>enable
Switch#
Global configuration mode: used to configure for parameters that apply the entire switch
Switch#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#
e.g. configuring a hostname
Switch(config)#hostname Testswitch
Testswitch(config)#
Use tab to complete a command
Testswitch(config)#int<tab>

## Slide 29: Interface configuration
Configuring an interface, from gloabal configuration mode, use interface <interface_type> <interface_no>
  Testswitch(config)#interface fastEthernet 0/1
  Testswitch(config-if)#
  To exit from the interface configuration mode, use exit
  Testswitch(config-if)#exit
  Testswitch(config)#
  e.g. to shut down fast ethernet 0/2, use
  Testswitch(config)#interface fastEthernet 0/2
  Testswitch(config-if)#shutdown
  %LINK-5-CHANGED: Interface FastEthernet0/1, changed state to administratively down
  Testswitch(config-if)#exit
  Testswitch(config)#exit
  Testswitch#

## Slide 30: Verification
Use show commands (from privileged mode)
Testswitch#show running-config
Testswitch# sh startup-config
And look at the modifications we made: hostname and fa0/2
Testswitch#sh ip interface brief
      Interfaces in brief
Testswitch#sh interfaces fastEthernet 0/2
      Interface detailed information
Testswitch#sh history
Use ? After the show command to see the possible lists of commands
Testswitch#show ?

## Slide 31: Password configuration
Enable password: access to privileged mode
Testswitch#conf t
Testswitch(config)#enable password ?
7 Specifies a HIDDEN password will follow
LINE The UNENCRYPTED (cleartext) 'enable' password
level Set exec level password
Testswitch(config)#enable password cisco
Now exit and login again
Enable secret: more secured
Testswitch(config)#enable secret cisco123
Now exit and login again

## Slide 32: Line configuration
Configuring password for console port
Testswitch(config)#line console 0
Testswitch(config-line)#password 123
Testswitch(config-line)#login
Now logout and login again!

## Slide 33: Saving Configuration
Unless saved, the running configuration will be lost if the switch boots (or if power goes off)
Contents of RAM copied to NVRAM
Testswitch# copy running-config startup-config
OR use write command from privileged mode
Testswitch#write

## Slide 34: Undo a command
Use “no” command before the command we want to remove.
E.g. to enable the fa0/2 we all ready shut down, and hostname of the switch, use
  Testswitch#
  Testswitch#conf t
  Testswitch(config)#int fastEthernet 0/2
  Testswitch(config-if)#no shutdown
  Testswitch(config-if)#exit
  Testswitch(config)#no hostname
  Switch(config)#

## Slide 35
User
mode
Privileged
mode
Global config
mode
Interface
Config mode
Line config
mode
enable
Conf t
Int <type> <no>
Line <type> <no>
exit
exit
exit
exit
Traversing between modes

## Slide 36: Reminders
Use the context-sensitive help (“?”) to list the possible commands
Do not forget to save your configuration
Keep Practicing and Practicing!!!!!!!

## Slide 37: VLAN
To create smaller broadcast domains within a layer 2 network
Treated as its own subnet or broad cast domain
Router needed for hosts on different vlans to communicate
Enhance network security
Segment broadcast domain->efficiency
PC1
PC2
PC3
PC4

## Slide 38: Configurations of vlans
VLANs are identified by a number from 1 to 4094
To configure VLAN,
  Switch(config)#vlan <vlan_id>
  Switch(config-vlan)#name <text>
  E.g. Switch(config)#vlan 10
  Switch(config-vlan)#name ICT
To delete a given VLAN
  Switch(config)#no vlan <vlan_id>
  e.g Switch(config)#no vlan 10

## Slide 39: Layer 2 Interface Modes
Access: if a port belongs to a single VLAN
Trunk: a switch port that carries multiple vlans
  E.g. A link between two switches
  ISL: proprietary to Cisco, used on old versions
  Dot1Q: standard for tagging vlans
switchport mode access: set to permanently access
switchport mode trunk: set to permanently trunk
switchport mode dynamic desirable: a port becomes trunk if the other end is trunk, deirable or auto
switchport mode dynamic auto: a port becomes trunk if the other end is trunk, deirable

## Slide 40: Cont’d
Switch(config)# interface gigabitethernet0/1
Switch(config-if)# switchport mode access
Switch(config-if)# switchport access vlan 10
Switch(config)# interface gigabitethernet0/2
Switch(config-if)# switchport mode trunk
Switch(config-if)# switchport trunk allowed vlan 1,10

## Slide 41: VTP
To manage all configured VLANs
Additions, deletions of vlans made on one central device and propagate through VTP
Three mode: Server, Client, Transparent
Uses configuration revision number to update vlan database

## Slide 42: Spanning Tree Protocol
Switches forward broadcast packets out all ports
Redundant connections are also necessary
Sw1
Sw2
Sw3
PC1
broadcast
Solution: STP to remove redundant links at layer2

## Slide 43: STP (Cont’d)
Use BPDUs to discover loops and select the root bridge
All switches find the best path to root bridge and block all redundant links
Bridge ID
Default priority-32768
The lower bridge ID the better
Priority
MAC address

## Slide 44: Election of root bridge
1. Elect the root bridge
  The switch with lower brige ID wins
2. Switch finds lowest cost path the root bridge
  Link costs
    100Mbps:19
    1Gbps:4
Three port roles
  Root port: used to reach the root bridge
  Designated port: forwarding port: 1 per link
  Blocking: blocked by STP

## Slide 45: Example 1
Switch A
Switch C
Switch B
All links are fast ethernet
32768:aaaa.aaaa.aaaa
32768:bbbb.bbbb.bbbb
32768:cccc.cccc.cccc
Q: Determine the port to be blocked.

## Slide 46: Example 2
Switch A
Switch D
Switch B
Switch C
All links have equal cost
4096:9999.9999.9999
32768:0101.0101.0101
8192:cccc.cccc.cccc
32768:dddd.dddd.dddd
Q: Determine the port to be blocked.

## Slide 47: Example 3
Switch A
Switch B
Fa0/1
Fa0/2
Fa0/10
Fa0/8
32768:5F30:EEEE.3D21
32768:5F30:FEEE.3D50
Q: Determine the port to be blocked.

## Slide 48: Configuration of STP
Cisco switches run PVST- 1 root bridge for each VLAN
To configure spanning tree
Switch(config)#spanning-tree mode pvst
To make a switch a root bridge
Switch(config)#spanning-tree vlan 1 root primary
To change a priority
Switch(config)#spanning-tree vlan 1 priority 4096

## Slide 49: Port states
Listening: switch sends/receives BPDU
Learning: learns MAC address
Forwarding: sending traffic
Blocking: stays in this state before moving to listening state

## Slide 50: Access Control List (ACL)
filters network traffic by controlling whether packets are forwarded or blocked at the router’s interface
List of permit and deny statements
Used for:
  Access control
  Filtering traffic
Rules:
  List is read from top to bottom and stops at the first match
  Implicit deny at the bottom
  Applied to an interface inbound or outbound

## Slide 51
Increase network performance
provide for security
  which traffic is blocked
  which traffic is forwarded
Uses src/dst addresses, protocol types (TCP, UDP or IP), port numbers to classify network traffic
ACL (cont’d)

## Slide 52: Types
Standard ACL:
  Matches based on source address
  Lower processor utilization
Extended ACL:
  Matches based source/destination address, protocol, source/destination port numbers
  Higher processor utilization
  Relatively complex syntax

## Slide 53: Configuration
Create the ACL
Apply to an interface
  inbound or outbound
Verify configuration
  Use show access-lists

## Slide 54: Configuration (cont’d)
Configuring standard access list
Router(config)#access-list <1-99> <permit/deny> <src address> <wild card>
E.g:
R1(config)#access-list 1 permit 192.168.1.0 0.0.0.255
  Access list 1 when applied will allow the network 192.168.1.0/24
R1(config)#access-list 1 deny host 192.168.1.1
  Will deny only 192.168.1.1 ip address
R1(config)#access-list 1 deny any
  Will deny any network

## Slide 55: Configuration (cont’d)
Configuring Standard access control list
access-list <100-199> <permit|deny> <protocol> <source-address> <source-wildcard-mask> <destination-address> <destination-wildcard-mask> <eq | lt| gt> <port-number>
E.g.
  access-list 101 permit ip 192.168.10.0 0.0.0.255 67.10.10.5 0.0.0.0
    Permits all ip connections from 192.168.10.0 network to a host 67.10.10.5
  access-list 101 deny tcp 192.168.10.10 0.0.0.0 67.10.10.5 0.0.0.0 eq 80
    Denies web access from host 192.168.10.10 to web server of 67.10.10.5

## Slide 56: Applying ACL
Either inbound or outbound
Use ip access-group <acl-number> <in | out>
E.g.
  Int fa 0/0
  Ip access-group 1 in applies acl number 1 on fa0/0 for inbound traffic
  Int fa 0/1
  Ip access-group 1 out applies acl 1 on fa 0/1 for out bound traffic

## Slide 57: Network Address Translation(NAT)
IPV4 address depletion: Private and Public
NAT is a translation b/n private and gloabal IP addresses
NAT has made IPV4 stay on the protocol list
Allows for multiple devices to share an IP address (global)
It also hides private IP addresses: enhances security

## Slide 58: Types of NAT
Static: one-to-one mapping between local and global addresses
  Usually for servers accessible from the Internet
Dynamic: translate private IP address to a pool of global IP addresses
Overload: maps multiple private IP addresses to a single global IP address
  Most popular
  Uses port Nos (Port Adress Translation or PAT)

## Slide 59: Configuration
Interfaces: the router/firewall needs to have at least two interfaces
  Inside: connects to our internal network
  Command used: ip nat inside
  Outside: connects to the external/Internet network
  Command used: ip nat outside
Static NAT:
  ip nat inside source static <private_IP><global_IP>
  E.g:
  ip nat inside source static 10.128.5.16 213.55.94.36

## Slide 60: Configuration (Cont’d)
Dynamic ACL:
  First select the private IP address to be translated
    Access-list 1 permit 10.128.0.0 0.0.255.255
  Create the pool of global IP addresses
    Ip nat pool <pool_name> <start_IP> <end-IP> netmask <subnet_mask>
    Ip nat pool mypool 97.10.50.1 97.10.50.30 netmak 255.255.255.224
  To translate
    ip nat inside source list <acl_no> pool <pool_name>
    Ip nat inside source list 1 pool mypool

## Slide 61: Configuration (Cont’d)
PAT (overloading):
  First select the private IP address to be translated
    Access-list 1 permit 10.128.0.0 0.0.255.255
  Overload it to outside interface
    ip nat inside source list 1 interface <interface_type> <interface_number> overload
  OR Overload it to one global ip address
  For verification
    sh ip nat translations

## Slide 62: Introducing Routing
Routers must learn the direction to remote networks in order to forward packets.
There are 2 ways to learn this information:
  Dynamic Routing
  Static Routing
Routers use the routing process to
  Forward packets toward the destination network
  Decisions based upon the destination IP address
Dynamic routing
  Routers learn information from other routers
  Scalable – each change learned from another router
Static routing

## Slide 63: Static Routing
Configured manually by the network administrator
  Add and remove static routes when topology changes
Static Route Operations are divided into three parts:
  Network administrator configures the route
  Router installs the route in the routing table
  Packets are routed using the static route
Command
  Router#config terminal
  Router(config)#ip route 172.16.1.0 255.255.255.0 s0
  Router(config)#ip route destination subnet outgoing

## Slide 64: Static Routes using Outgoing Interface
Specifies
Outgoing
Interface

## Slide 65: Static Route Using Next Hop
Specifies
Next Hop

## Slide 66
The Difference between the 2 options is
  Administrative distance assigned to the route
Administrative distance
  Optional
  Measures the reliability of the route (0 – 255)
  The lower the number the more reliable the route
  Set to 1 for next hop
  Set to 0 for outgoing interface
Routers choose the route with the lowest administrative distance
The Difference between the 2 options is

## Slide 67
  ip route 192.21.121.0 255.255.255.0 192.21.122.1 130
Static routes
  Can be used as a backup if dynamic route fails
  Must have higher admin no. to dynamic route
To set a static route that is not 1 or 0

## Slide 68: Configuring a Default Route
Default routes
  Route packets with destinations that do not match any of the other routes in the routing table
  Often used for
    internet-bound traffic
    Non-directly connected networks
Special form of a static route
  ip route 0.0.0.0 0.0.0.0 [next-hop-address or outgoing if]
  Example ip route 0.0.0.0 0.0.0.0 s0

## Slide 69: Verifying static route configuration
show running-config
  Views the active configuration in RAM to verify that the static route was entered correctly
show ip route
  Make sure that the static route is present in the routing table
Ping <ip address>
  check a connection
Traceroute <ip address>
  Shows the path to the ip address
    Can be used to identify where the connection fails